# Overview
## Description
Hobark Makers have a K40 laser cutter/engraver. These are a common, low cost, Chinese sourced laser capable of engraving and cutting a numbe of materials. As supplied, the controller and software limited and electrical safety was not high on the designers list of requirements. Because of these factors, it’s been modified (we’re makers, that’s what we do...)
## Modifications
Our K40 is far from stock. The original owner removed the standard Coreldraw based controller and added an Arduino and the whole thing was controlled by Linuxcnc.
Currently the controller is a Raspberry Pi Model B+ with a Protoneer Rpi-CNC hat attached. The Raspberry Pi runs Laserweb4 and the Protoneer Arduino runs grbl 1.1h.
The steppers are drive by M542 stepper motor controllers, one for each of X and Y axis (Z axis could be added at some future point).
A recent rebuild has been done to address a number of issues, mostly to tidy up the wiring and to improve safety where required and to provide a few feature upgrades.
The standard power supply provides the high tension voltage for the laser tube as well as 24V for the stepper drivers and 5V for control logic. Several posts on https://forum.makerforums.info/ point out that this supply, while sufficient for the high tension requirements, is lacking in power for the stepper drivers. For this reason, a separate 24V supply has been fitted. This supply also provides 5V for the Raspberry Pi. There’s also a 12V rail for use as required – currently this is to control the SSR’s and LED lights.
Two SSRs have been added to control power to the exhaust fan and to the air assist pump. These are operated by switches added to the front panel. Air assist can also be operate on demand by Laserweb4 although this will require some extra components.
A water flow switch has been added so that the laser will not fire if water is not flowing through the laser tube.
A new pump has been added with a larger coolant tank (it’s a beer keg because, why not?) along with a probe for coolant temperature monitoring (to be added)
The Makers github has all the circuit diagrams of the modifications and various images and notes to help should anyone else want to make changes/improvements.
### Possible Upgrades include:
- Add interlock switches to the various opening panels for added user security.
- New control panel which support for interlocks, water flow and temperature monitoring
- More bling!