4 Pin Connector to Powet
L	Earth fro laser tube cathode
FG	Chassis ground
AC	active
AC	neutral

6 Pin Connector To Control Panel
G1	0
P1	0	G1 and P1 may be swapped, check!
L1	0	Connected to L1 on 4 pin connector,Low to enable
G1	0	To potentiometer
IN	Centre pin	To potentiometer
5V	0	Supply to potentiometer only

4 Pin Connector to Controller
24V	0	0
G1	0
5V	0	0
L1	0	Connected to L1 on 6 pin connector, low to enable