<Alarm|WPos:231.281,176.055,0.000|FS:0,0|Pn:Z|WCO:-231.281,-176.055,0.000>
Variable	Value	Description
$0	10	Step pulse, microseconds
$1	255	Step idle delay, milliseconds
$2	0	Step port invert, mask
$3	3	Direction port invert, mask
$4	0	Step enable invert, boolean
$5	1	Limit pins invert, boolean
$6	0	Probe pin invert, boolean
$10	0	Status report, mask
$11	0.010	Junction deviation, mm
$12	0.002	Arc tolerance, mm
$13	0	Report inches, boolean
$20	0	Soft limits, boolean
$21	0	Hard limits, boolean
$22	1	Homing cycle, boolean
$23	1	Homing dir invert, mask
$24	250.000	Homing feed, mm/min [25]
$25	1000.000	Homing seek, mm/min [500]
$26	250	Homing debounce, milliseconds
$27	5.000	Homing pull-off, mm
$30	1000	Max spindle speed, RPM
$31	0	Min spindle speed, RPM
$32	1	Laser mode, boolean
$100	160.000	X steps/mm
$101	160.000	Y steps/mm
$102	250.000	Z steps/mm
$110	1000.000	X Max rate, mm/min [5000]
$111	1000.000	Y Max rate, mm/min [5000]
$112	500.000	Z Max rate, mm/min [500]
$120	10.000	X Acceleration, mm/sec^2 [50]
$121	10.000	Y Acceleration, mm/sec^2 [50]
$122	10.000	Z Acceleration, mm/sec^2 [10]
$130	300.000	X Max travel, mm
$131	300.000	Y Max travel, mm
$132	200.000	Z Max travel, mm